## Slide 1: Nuclear reactor model for axial offset control
Nikolas Chung
Supervisors: Christos Evripidou, Dr Mehmet Mercangoz
UROP PROJECT

## Slide 2: Outline
01
What is this project, and why?
02
From references to model structure
03
Background: reactor physics
04
What exactly are we controlling?
05
Live demo
06
Model validation
07
Model constraints
08
Final notes

## Slide 3: What is this project, and why?
Intrinsic motivation: nuclear energy, PDC
Extrinsic motivation: the renaissance of nuclear energy
Goal: a Python platform for experimenting with control strategies for nuclear energy systems in load following.
01 · MOTIVATION

## Slide 4: Who is this project useful for?
01 · MOTIVATION
01
Audience
Control-oriented researchers. Core idea: build, plug, run.
02
Approach
A simple API and interactivity. Only limited background in nuclear reactor analysis is needed.
03
Status
Still a little rough around the edges: some parts still need validation, and the UX can be polished further.

## Slide 5: What makes this control problem interesting?
Uranium → iodine → xenon (xenon is a very strong neutron absorber)
1
3.65m
3.02 m
2
01 · MOTIVATION

## Slide 6: Model structure: what makes it different?
Two-point core: Li (2014)
Plant: Vajpayee et al. (2020)
Why 2 coolant nodes? →
Plant based on the H. B. Robinson PWR (Kerlin et al., 1976)
02 · MODEL STRUCTURE

## Slide 7: Background: the chain reaction
Fission: neutrons are born fast (high energy) and are slowed down by the coolant until they are thermal (low energy).
Thermal neutrons are reabsorbed in the fuel, and the chain reaction continues.
It is all about controlling the chain reaction.
03 · BACKGROUND

## Slide 8: Reactivity and criticality
Reactivity ρ measures how far the core is from criticality.
Reactor state | ρ (reactivity) | (criticality)
Steady state | 0 | 1
Supercritical | > 0 | > 1
Subcritical | < 0 | < 1
Reactor state | ρ (reactivity) | 
Steady state | 0 | 1
Supercritical | > 0 | > 1
Subcritical | < 0 | < 1
03 · BACKGROUND

## Slide 9: What changes reactivity?
Increases reactivity ↑ | Decreases reactivity ↓
Coolant temperature decreases | Coolant temperature increases
Fuel temperature decreases | Fuel temperature increases
Less boron | More boron
Control rods withdrawn | Control rods inserted
Less xenon | More xenon
Primary-side explanation →
03 · BACKGROUND

## Slide 10: Control example: load disturbance
FC
UTG
First: what happens on the secondary side?
04 · CONTROL PROBLEM

## Slide 11
Reactivity reference →
Coolant temperature rises and coolant becomes less dense
→ reactivity decreases
Fuel temperature decreases
→ reactivity increases
The reactivity effects cancel, so Tavg takes a long time to settle
04 · CONTROL PROBLEM
On the primary side, it is more complicated

## Slide 12: Therefore, control rods are needed
04 · CONTROL PROBLEM

## Slide 13
04 · CONTROL PROBLEM
Axial offset over a 24-hour load-follow cycle

## Slide 14: Demo time
Search for the GitHub repo
05 · LIVE DEMO

## Slide 15: Validation against Vajpayee et al. (2020), Fig. 10
06 · VALIDATION
Open-loop test cases
Case A rod / reactivity step (state step)
Case B valve coefficient +5 %
Case C heater +50 %, 20–100 s
Case D feed-water temperature ramp
Perturbation applied at t = 20 s
Published (Vajpayee et al., 2020)
This model

## Slide 16
06 · VALIDATION
Validation against Vajpayee et al. (2020), Fig. 11
Open-loop test cases
Case A rod / reactivity step (state step)
Case B valve coefficient +5 %
Case C heater +50 %, 20–100 s
Case D feed-water temperature ramp
Perturbation applied at t = 20 s
Published (Vajpayee et al., 2020)
This model

## Slide 17: What is missing, and what the model is not
07 · MODEL CONSTRAINTS
Still to validate
Against Li’s model (diffusion / coupling parameter)
Recreate the MATLAB/Simulink solvers to validate against Vajpayee et al.
Out of scope
Start-up and shut-down
Thermal limits (peaking factors)
Radial offset
…and more, documented in validation_notes.md

## Slide 18: Special thanks
Dr Mehmet Mercangoz, Christos Evripidou, Li Qu, Javal, fellow UROPs Marco and Nas, and everyone for being so welcoming and supportive!
08 · FINAL NOTES

## Slide 19: References
Kerlin, T.W., Katz, E.M., Thakkar, J.G. and Strange, J.E. (1976). Theoretical and experimental dynamic analysis of the H. B. Robinson nuclear plant. Nuclear Technology, 30(3), pp. 299–316. doi:10.13182/NT76-A31645.
Li, G. (2014). Modeling and LQG/LTR control for power and axial power difference of load-follow PWR core. Annals of Nuclear Energy, 68, pp. 193–203. doi:10.1016/j.anucene.2014.01.022.
Vajpayee, V., Becerra, V., Bausch, N., Deng, J., Shimjith, S.R. and Arul, A.J. (2020). Dynamic modelling, simulation, and control design of a pressurized water-type nuclear power plant. Nuclear Engineering and Design, 370, 110901. doi:10.1016/j.nucengdes.2020.110901.

## Slide 20
A simplified core heat-transfer model (1 fuel node, 2 coolant nodes) closely tracks the detailed model (15 fuel nodes, 30 coolant nodes).
Shown: change in reactor outlet temperature and reactor power.
Source: Kerlin et al. (1976)
← Back
APPENDIX
Backup: why two coolant nodes?